## Slide 1: Airline Fleet Assignment with Homogeneity
Jacques Desrosiers
HEC & GERAD
Montréal, Canada

## Slide 2: COLLABORATORS
Nicolas Bélanger
Guy Desaulniers
François Soumis
GERAD
June Lavigne
Air Canada

## Slide 3: AIRLINE PLANNING PROCESS
Fleet Planning
Crew Planning
Flight Scheduling
MTL TOR
7.00 7.50 MTWTFSS
8.00 8.50 MTWTFS -
9.00 9.50 MTWTFSS
...

## Slide 4: AIRLINE PLANNING PROCESS
Flight Scheduling
Fleet Planning
Crew Planning
FLEET ASSIGMENT
aircraft type --> flight
AIRCRAFT ROUTING
sequence of flights
for each aircraft

## Slide 5: AIRLINE PLANNING PROCESS
Flight Scheduling
Fleet Planning
Crew Planning
CREW PAIRING
base-to-base rotations
CREW ROSTERING
monthly blocks

## Slide 6
FLEET PLANNING
FLEET ASSIGMENT
aircraft type --> flight
AIRCRAFT ROUTING
sequence of flights
for each aircraft
Integrated Model
for Large Scale
Weekly Problems
Max PROFIT + QUALITY
st: Flight Covering
Flow Conservation
Connection Times

## Slide 7: PROFIT = REVENUES - COSTS
Passenger Routing
Stochastic Variation of the Passenger Demand

## Slide 8: PROFIT = REVENUES - COSTS
Passenger Routing
Fixed Routing:
Variable Routing: a Game Theory Model

## Slide 9: PROFIT = REVENUES - COSTS
Stochastic Variation of the Passenger Demand
Aircraft Capacity

## Slide 10: PROFIT = REVENUES - COSTS
the aircraft type
the distance between cities
the direction (East/West winds)
Cost of a leg
is a function of

## Slide 11
The proposed model uses
fixed passenger routing
The passenger routing
can be readjusted
by using an external loop
Revenues from assigning an aircraft to a leg
are evaluated by a preprocessor

## Slide 12: QUALITY FACTORS
Global : many flights
Local : a single flight or a connection
Easy to include into the model

## Slide 13: QUALITY FACTORS
Global : many flights
Local : a single flight or a connection
More difficult to include into the model

## Slide 14: QUALITY FACTORS
Penalty on short connections to improve robustness
Local : a single flight or a connection
Easy to include into the model
Preferences on aircraft type for ground service availability

## Slide 15: QUALITY FACTORS
Global : many flights
More difficult to include into the model
Homogeneity of aircraft type for a flight number over a week :
reduces ground service costs and improves customer service

## Slide 16: Time-space Network for Aircraft Type k
City A City B City C

## Slide 17: Integer Variables
flight variable: binary
ground variable: non negative
aircraft number: non negative
dominant aircraft type: binary
(non) homogeneity variable: non negative

## Slide 18: Mathematical Model
Profit per leg l
per aircraft type k
Fixed cost per aircraft type k
Penalty factor for non-homogeneity

## Slide 19: Mathematical Model
Selection of an aircraft type k
for each leg l

## Slide 20: Mathematical Model
Selection of a
dominant aircraft type k
for each flight number f(l)

## Slide 21: Mathematical Model
Computation for non-homogeneity
for each aircraft type k
and for each leg l

## Slide 22: Mathematical Model
Flow Conservation (k  K) Aircraft Count (k  K) Integer Variables
Remaining constraints

## Slide 23: Mathematical Model
Flow Conservation (k  K) Aircraft Count (k  K) Integer Variables

## Slide 24: SOLUTION APPROACHES
DIRECT
TWO PHASES

## Slide 25: SOLUTION APPROACHES
DIRECT
Integer Linear Programming
B&B on binary variables
and
 other variables become integer
Small integrality gaps
Stop at the first integer solution

## Slide 26: SOLUTION APPROACHES
TWO PHASES
.- Select dominant aircraft types on a less than 7-day problem
.- Over the week, select dominant aircraft types for the remaining flights and optimize the aircraft routing

## Slide 27: Air Canada data (10 aircraft types)

## Slide 28: Trade-off: Homogeneity vs Profits

## Slide 29: Trade-off: Homogeneity vs Profits

## Slide 30: Two-Phase Approach
Solution times can be reduced significantly without deteriorating the quality of the solutions in terms of anticipated profits and homogeneity
Data Set 2
(4 days)

## Slide 31: Comparison with Air Canada
Data Set 2
(4 days)

## Slide 32: Comparison with Air Canada
241, 0%

## Slide 33: CONCLUSIONS
OPERATIONS
STRATEGIC PLANNING

## Slide 34: CONCLUSIONS
STRATEGIC PLANNING
Scenarios
can be compared
without
manual adjustments
Effect of adjustments on profit
is very small
Opens the way to study many scenarios
in a small amount of time

## Slide 35: CONCLUSIONS
Human intervention needed to adjust some details
Solutions close to optimality
Human intervention needed to adjust some details
Solutions close to optimality
Human intervention needed to adjust some details
Solutions closer to be operational ...
OPERATIONS
System produces solutions that meet expectations of planners
Very good productivity
Local and global quality factors

## Slide 36: Airline Fleet Assignment with Homogeneity